## EQU: equilibrium composition of a fluid-rock system
Having considered the case of homogeneous equilibrium state of an aqueous fluid under composition / potential constraints, we consider now the equilibrium state of a system that may comprise, in addition to the aqueous phase, non-aqueous phases such as minerals or gases.
Among the non-aqueous phases considered potentially present, we call hereafter "active phases" those at equilibrium and "inactive" the others.
To the equation system describing the homogeneous equilibrium of the aqueous phase, there is, for each active phase:
▶ an additional unknown: its mole number, which enters in the material balance equations,
▶ an additional chemical potential equation: its equilibrium condition with the aqueous phase.
To compute the composition of the system at equilibrium, ARXIM uses an iterative method that is classical for mineral / fluid equilibrium in the LMA way (e.g. EQ6, Wolery, 1979). The speciation of the aqueous phase plays the central role, as it is called at each iteration for computing the disequilibrium degree between water and other phases considered in the chemical space.
The scheme is as follows, starting with an arbitrary set of active phases:
given the amounts of aqueous phase and other active phases
do:
  1. solve for equilibrium state with the current active phase set

  2. if any active phase has a negative mole number:
    make inactive that phase with the most negative mole number
    cycle

  3. if any inactive phase is super-saturated versus aqueous phase:
    3a. activate (add) the most super-saturated
    3b. inactivate (remove) any active phase in conflict
    cycle

  exit
Similar iterative scheme are used in water-rock interaction codes such as CHESS (van der Lee, 1998), or GWB (Bethke, 1996), but, at variance with GWB or CHESS, the non-aqueous active species are not swapped into the set of primary species for equilibrium conditions.
The main difficulty with this scheme lies in step 3b, if the new phase happens to be compositionally dependent of the current active set and the question arises of which active phase should leave the active set. If there is dependency, we can compute the stoichiometry of the formation of the new phase from the currently active phases, and the phase to be removed will be the phase i with the lowest Xi / νi , where Xi is the mole number of phase i and νi its coefficient in the reaction of formation of the new phase.
### equilibrium involving mixtures
When mixture phases (gas mixtures, solid solutions) are considered as potentially entering the active set, their compositions are additional unknowns, but the same scheme can be adapted as follows:
At step 3, when computing the saturation degree of all possible phases, we compute, for each mixture, the mixture composition that gives the maximum super-saturation with respect to the current aqueous composition. The most super-saturated mixture phase, if any exists, is added, as a pure phase with this composition, to the set of phases considered in 3a. If, on next loop, a mixture enters the active set, its composition is adjusted by iterating step 1 (convergence is reached in 2-3 iterations).
next: examples of equilibrium calculations