## ARXIM / SPC: the speciation of an aqueous fluid
The question of speciation is central in aqueous chemistry. The development of a robust speciation solver is thus essential for most simulations of fluid-rock interactions.
Solving a speciation problem is typically the calculation of the homogeneous thermodynamic equilibrium of a mixture phase that follows an asymmetric solution model, giving rise to homogeneous reaction between species. For speciation calculations, the thermodynamic system under consideration is a given amount of aqueous solution (for example, corresponding to 1 kilogram water), in a given environment that controls temperature, pressure, and eventually, through heterogeneous equilibrium with other phases, the chemical potentials of some components.
The solution of a speciation problem involves the implementation of the two types of constraints, on chemical compositions ("material balance" constraints) and on chemical potentials ("mass action" constraints, which are "potential balance" constraints).
In the case of a closed system, given N independent components of known mole numbers c(1:N), and M chemical species with given stoichiometric / thermodynamic properties, we have to determine how the N components are distributed among the M species.
### material balance constraints: choice of components
Various approaches are possible for selecting the set of independent components used for the description of composition constraints.
#### the "basis species" approach ("Morel tableau")
One approach is to use chemical species as components. A set of linearly independent species ("basis species", or "component species", or "primary species") is selected, which will be the "basis" against which the stoichiometry of the other species is described.
This approach seems the most "natural" for an homogeneous closed system; one of its advantage is to use a minimum number of variables to describe both the stoichiometry and the chemical equilibrium of the system. Moreover, it allows a compact formulation of the speciation problem: the mass action relations expressing the "secondary species" as explicit functions of the primary ones can be substituted in the material conservation equations, giving a system with a minimal number of equations, one for each "primary species".
This approach is well suited for equilibrium calculations of an homogeneous system, e.g. purely aqueous, but it can make more complex the solution of "open system speciation" problems.
It is to note that, in this approach, the role of a basis species is twofold: it is both a component involved in the stoichiometric description of the mass balance and a chemical species involved in mass action relations. The denomination of "component species" better emphasizes this duality.
Consequently, a "basis species" is assigned two types of abundances: a true "chemical" abundance relevant to the chemical species itself, and a "total" or "generalized abundance" for the corresponding "component species" (Lichtner, 1996).
##### Example
For a carbonate-bearing aqueous solution with six chemical species considered potentially present (H2O, H+, HO-, CO2, HCO3-, CO3-2), we can select {H2O,H+,CO2} as basis and describe HO- as (1,-1,0), HCO3- as (1,-1,1), CO3-2 as (1,-2,1).
The mass balance relation for "total carbonate" will be, in mole numbers:
n_total(CO2) = n(CO2) + n(HCO3-) + n(CO3-2)
#### the elements as components
The "basis species" set correspond to a particular choice of "independent components", but, as already pointed out, thermodynamic components do not necessarily correspond to any species' stoichiometry; they only have to form a set of linearly independent entities that can generate the whole "chemical space" defined by the species under consideration.
Moreover, it is not necessary to use the same component set in the two sets of constraints, on compositions and on potentials respectively. In the "basis species" case, the two component sets apparently coincide, but the same "species" is actually used as a stoichiometric substance in one set, and as a chemical species in the other.
In ARXIM, we chose the apparently most "basic" option, which is to use as components, for the implementation of material conservation, the chemical elements present in the system.
In the case of an aqueous system, where the component set should be able to describe ionic species, the electron (or the electronic charge) has to be considered as a component, but a peculiarity of this "charge component" is that it is generally assigned a total balance of zero, because we assume that electrolytic solutions are at electrostatic equilibrium.
For example, considering a carbonate-bearing aqueous solution with six chemical species (H2O, H+, HO-, CO2, HCO3-, CO3-2), a "basis" composed of the four components (O,H,C,Chg) describe the species compositions using the following stoichiometric table
      O H C Chg
H2O 1 2 0 0
H+ 0 1 0 +1
CO2 2 0 1 0
HO- 1 1 0 -1
HCO3- 3 1 1 -1
CO3-2 3 0 1 -2
We obtain here the "formula table" of the system, where each species is represented by its "formula vector", e.g. the line vector (1,2,0,0) for H2O.
#### accounting for redox state
From the stoichiometry of the species listed in the former example, it appears that only one oxidation state has been considered for each element. Actually, an element list such as { O[-2], H[+1], C[+4] }, would state more explicitly the oxidation state considered for each element in this example.
The oxidation state of an element is directly deduced from the stoichiometry of the species it enters in. The method can be explained with the example of the carbonate system: to account for the presence of species H+, H is assigned the oxidation state [+1]; as a result, O is assigned the state [-2], because of the presence of OH- or H2O; finally, element C must be assigned the state (+4), to be consistent with the charge of three species it forms with O[-2] and H[+1].
By making the oxidation state an intrinsic property of the "element component", it is possible to have a full description of the system's stoichiometry without resorting to an additional "charge" component. In order that the solution of the speciation problem satisfies the electro-neutrality equation (the global balance of the species' charges is null), the global balance of the elements' valencies must be zero.
If we consider now an aqueous system where reduced and oxidized species (e.g. CH4, H2, O2) are potentially present, then we have to introduce an additional component, a "redox component" (component called "Ox" in ARXIM), which describes the oxidation state of the different species with respect to the "default oxidation state" of the elements.
The following table is obtained:
      O H C Ox (Chg)
vVal -2 1 4 1 -1
H2O 1 2 0 0 0
H+ 0 1 0 0 1
CO2 2 0 1 0 0
HO- 1 1 0 0 -1
HCO3- 3 1 1 0 -1
CO3-2 3 0 1 0 -2
O2 2 0 0 4 0
H2 0 2 0 -2 0
CH4 0 4 1 -8 0
Here, the vector line vVal, which contains the default oxidation states, is not a part of the formula table, but rather a property assigned to the respective element components.
The value of the redox component Ox of a species in a system will depend on the choice of the default values of the oxidation states of elements.
#### equations for material balance constraints
There are as many material balance constraints as inert components.
The formula matrix α(1:nC,1:nAq) of the whole system describes the stoichiometry of all aqueous species in terms of the elements.
The material conservation is expressed by nC equations of the form:
%PSI_{i in C} = sum _{j in Aq} (%alpha_i^j . bold n_j) - bold b_i " " = " " 0
with
▷ b(1:nC) the mole numbers of inert components,
▷ n(1:nAq) the mole numbers of aqueous species ({Aq} = index set of aqueous species,
▷ α(1:nC,1:nAq) the species' formula matrix.
##### case of aqueous species of fixed potential
When mobile aqueous species (species index set Ax) are present, their contribution to the mole balance of component i can be separated from that of the inert aqueous species (species index set Ai).
sum _{ j in Ai} (%alpha_i^j . n_j) " " + sum _{j in Ax} (%alpha_i^j . n_j) " " - b_i " "= 0
Here, the mobile species abundances can be calculated from their (fixed) activities if their activity coefficients (γ) and the solvent abundance are known:
n_i = m_i n_w M_w " " drarrow " " n_i = a_i over %gamma_i . n_w . M_w
where Mw is the molar weight (kg) of solvent.
In this expression, only nw, the solvent mole number, is unknown, because the activity coefficients γ(1:S), which depend on the solution composition and thermodynamic model, are held constant within the execution of the solver routine and calculated in an external loop.
"Equ"[i=1:nC]" : " sum _{j in Ai} { %alpha_i^j . n_j } " "+ n_w . M_w sum _{j in Ax} {%alpha_i^j . a_j over %gamma_j } " " - bold b_i = " " 0
### equilibrium constraints in closed systems
In a mixture where the number of species equals the number of independent components (case of "interaction" mixing models, common for minerals, melts, gases), the species abundances are completely determined by the phase composition and the species stoichiometry. But, if the phase follows a model of "association solution", each time an additional species is considered, an additional equation is provided by a chemical equilibrium condition, i.e. an "internal constraint" among the species' chemical potentials.
#### primary and secondary species
In a "LMA approach", the equilibrium condition of a closed system of {nC components, nAq aqueous species} is implemented as a set of independent mass action relations among the aqueous species.
The number of such independent reactions is nAq - nC. To write these reactions, it is convenient to split the species set into,
nC linearly independent "primary species",
nAq - nC "secondary species" whose formation (or dissociation) reactions are expressed in terms of the "primary species".
ARXIM follows an approach similar to LMA approaches, except that, instead of mass action relations expressed in terms of activity products, equilibrium is written as a set of linear relations between chemical potentials.
There are as many "basis species" as components, 3 in the example system {(H,O,C), (H+, H2O, CO2, HO-, HCO3-, CO3-2)}. The selection of the "primary species", as long as they form a basis for the system, is rather arbitrary. Practically, in aqueous systems, H2O is always chosen as primary species, for its role as solvent. It is also practical to have H+ (or OH- in basic conditions) as component, because of its central role in acid-base reactions. For other elements, the species with the highest dissociation degree (e.g. Na+ for Na, Ca+2 for Ca, PO4-3 for P) can be selected as the default primary species.
The primary species selection is arbitrary, but the program may modify the species set during speciation calculation, in order to have the most dominant species as primary species, which secure the numerical resolution of the problem. Such a systematic basis change is essential when the equilibrium conditions are formulated in terms of concentrations or mole numbers as variables; it is not critical when the formulation, as done in ARXIM, is in terms of their logarithms, which gives linear equilibrium equations.
In the case of open system, the mobile species are selected as primary species. This simplifies the expression of the equilibrium conditions: if a mobile species is not aqueous, its selection as primary species allows the implementation of equilibrium conditions with the same type of equations as those used for homogeneous equilibrium. The remaining inert "primary species" are selected among aqueous species that are independent from each other and from the mobile species.
#### example
For the system {(H,O,C), (H+, H2O, CO2, HO-, HCO3-, CO3-2)}, if (H2O, H+, CO2) is selected as "basis", the other species ("secondary species") are defined in relation with this basis by the following stoichiometry matrix ν(1:nS-nC, 1:nC), the same as that used for stoichiometry description in the pure "basis species approach":
       H2O H+ CO2
HO- 1 -1 0
HCO3- 1 -1 1
CO3-2 1 -2 1
#### stoichiometry of the reactions of formation of secondary species
If the basis species have been appropriately selected, then the matrix made of the primary species column vectors of the formula matrix, α(1:nC,iP), is non singular. Its inverse, which expresses the elements (1:nC) in terms of the basis species (1:nC), will constitute the "transformation matrix" used to compute the matrix νAs(1:nAs,1:nC) giving the stoichiometry of the aqueous nAs secondary species in terms of the nC primary species.
The same transformation matrix is used to compute the stoichiometry matrix νMs(1:nMs,1:nC) of non-aqueous species (species in minerals and gases).
The matrices νAs and νMs are also used for computing ΔG°As(1:nAs) and ΔG°Ms(1:nMs), the ΔG°'s of the formation reactions of all secondary species, respectively aqueous and non-aqueous.
#### equations for chemical potential constraints
If the system is at equilibrium, then nAs=nS-nC independent chemical reactions between the primary and secondary species are at equilibrium.
There are nAs chemical potential constraints, one for each secondary species:
%PSI_{js in As} " " = " " %mu_js " " - sum _{jp in Pr} {%nu_js^jp . %mu_jp } " " = " " 0
where
▷ µ(1:nS) is the array of the chemical potentials of all species of the system,
▷ {Pr} is the primary species set,
▷ {As} is the secondary species set,
the matrix υ(1:nAs,1:nC) describes the stoichiometry of the formation reactions of secondary aqueous species from primary species.
##### example: System {(H,O,C), (H+, H2O, CO2, HO-, HCO3-, CO3-2)}
Having selected (H2O,H+,CO2) as basis, the equilibrium conditions, ΔG=0, for the formation of the three secondary species yield the following relations:
Mu(HO-) = Mu(H+) + Mu(H2O)
Mu(HCO3-)= - Mu(H+) + Mu(H2O) + Mu(CO2)
Mu(CO3-2)= - Mu(H+) + Mu(H2O) + Mu(CO2)
where Mu(X) is the chemical potential of the species X.
The "reduced potential" µj (i.e. potential divided by R.T, which makes it dimensionless) is related with the activity of species j, aj, by the relation
%mu_j = %mu_j^0 + ln a_j
where µ°j is the reduced molar Gibbs enthalpy of species j in the reference state, calculated at (T,P) from data retrieved from the thermodynamic database.
The equilibrium conditions can be written as follows:
%PSI_{js in As} " = 0 = " ln a_js " " - sum _{jp in Pr} {%nu_js^jp . ln a_jp } " " - %DELTA G_js^0
where a(1:nAq) contains the activities of all species and ∆G°js is the "reduced" free energy change of the dissociation reaction of the secondary aqueous species js:
%DELTA G_js^0 = sum _{jp in Pr} {%nu_js^jp . %mu_jp^0 } - %mu_js^0
This formulation is equivalent to the classical "mass action" form, using "ion activity products" and "equilibrium constants", which is more common in aqueous geochemistry. In mass action form, the equilibrium condition for species js would become:
a_{js} = K_{js} prod _{jp in Pr} (a_jp) ^{%nu_js^jp} with K_{js} = exp(%DELTA G_{js}^0 )
#### relating potential constraints with material balance constraints
We have thus two sets of linear equations, one in species mole numbers, the other in species potentials. We have to relate the species' potentials with their mole numbers: that is the role of the mixing model to implement these "activity – composition" relationships.
##### in the case of aqueous solutions
In aqueous solutions, there is a dominant species, the "solvent" H2O, against which the concentrations of the other species, the "solute" species, are measured. The mixing model is asymmetric: solvent and solutes follow respectively a mole fraction and molality scale and have different forms of activity – composition relations.
▷ for the solvent, a_w = x_w . %lambda_w , where mole fraction x_w = n_w over {n_w + %SIGMA_{i<>w}n_j}
▷ for a solute species, a_j = m_j . %gamma_j , where molality m_j= n_j over {n_w . M_w}

We have thus a_{j<>w} = %gamma_j . n_j over {n_w . M_w}
The equilibrium condition between secondary species js and primary species (jp in {Pr}) comprises two terms, respectively for solvent species (w) and for other primary species,
%PSI_js = " " %nu_js^w . ln bold a_w + sum_{jp in Pr/w} (%nu_js^jp . ln bold a_jp) - ln bold a_{js} + %DELTA G°_{js} " "= 0
or, in terms of mole numbers of aqueous species, n(1:nAq):
alignl %PSI_js " = 0 = " newline alignl " " sum_{jp in Pr/w} (%nu_js^jp . ln bold n_jp) - ln bold n_{js} - [sum_{jp in Pr/w} %nu_js^jp - 1] . ln (bold n_w M_w) newline alignl " " + %nu_js^w . ln a_w + %DELTA ln %gamma_js + %DELTA G°_js " = 0"
where ΔLnγ_js is the "balance" of activity coefficients in the dissociation reaction of species js:
%DELTA ln %gamma_js = sum from jp<>w (%nu_js^jp . ln %gamma_jp) " " - ln %gamma_js
### implementation
#### the system of equations, closed system
For the nAq=nC+nAs unknown mole numbers of aqueous species, represented by the array n(1:nAq), we have a system of nC+nAs equations:
▷ nC material balance equations:
%PSI_{i in C}" = 0 = " sum _{j in Aq} {%alpha_i^j . bold n_j} " " - bold b_i
▷ nAs chemical potential balance equations:
alignl %PSI_{js in As} " = 0 = " newline alignl " " %nu_js^w . ln a_w + sum _{jp in Pr/w} (%nu_js^jp . ln bold n_jp) - ln bold n_js newline alignl " " - [sum_{jp in Pr/w} %nu_js^jp - 1] . (ln bold {n_w} + ln M_w) + %DELTA ln %gamma_js + %DELTA G^0_js
#### open system
For an open system comprising nCi inert and nCx mobile components (pointing respectively to index set {Ci} and set {Cx}, with nCi +nCx =nC), the system of equations is modified as follows:
▷ nCi material balance equations:
%PSI_{i in Ci} " = 0 = " sum _{j in Aq} {%alpha_i^j . bold n_j} " " - bold b_i
▷ nAq - nCi potential balance equations:
alignl %PSI _{js in As} " = 0 = " newline alignl " " %nu_js^w . ln bold a_w + sum _{jp in Ci/w} (%nu_js^jp . ln bold n_jp) - ln bold n_js newline alignl " " - [sum _{jp in Ci/w} %nu_js^jp - 1] . (ln bold {n_w} + ln M_w) + %DELTA ln %gamma_js + %DELTA G°_js newline alignl " " + sum _{jp in Cx} (%nu_js^jp . ln a_jp)
Thus, for an open system, compared to a closed system with the same number of aqueous species, the number of material balance equations decreases by the number of mobile components, whereas the number of secondary aqueous species, and thus of associated internal constraints on chemical potentials, increases by the same number.
For example, if all constraints but on the solvent are potentials of non-aqueous species, the system becomes:
%PSI_w " = 0 = " sum _{j in Aq} {%alpha_w^j . bold n_j} " " - b_w
alignl %PSI_{js in As} " = 0 = " newline alignl " " %nu_js^w . ln a_w - ln bold n_js - (ln bold {n_w} + ln M_w) newline alignl " " + %DELTA ln %gamma_js + %DELTA G°_js newline alignl " " + sum _{jp in Cx} %nu_js^jp . ln bold a_jp
#### resolution
This system of non-linear equations can be solved for the species' mole numbers, X(:)= n(1:nAq), or for their logarithms, which are homogeneous to the species affinities, the primary variables in the chemical potential equations.
When solving the system for X(:)= Ln(n(1:nAq)), the equilibrium equations are linear, but the conservation equations become sums of exponential terms, with possibly strong non-linearity.
The solvent activity aw and the activity coefficients of solutes, γj, are functions, generally non-linear, of the composition n. The system is solved by iteration: an internal loop, where the system is solved for Ln(n) with fixed values of the solute activity coefficients and the solvent activity, and an external loop that uses the composition n to update these parameters until convergence is attained between successive estimations of the activities.
The system is solved first on the Ln(n) array with an arbitrary value of the vΔLnγ(js) (for example zero, corresponding to a highly dilute solution); then the solution Ln(n) is used to compute a new set of ΔLnγ(js) that enters as constant terms in the residual system. The procedure is repeated until convergence on ΔLnγ(js). As a matter of fact, the variation of the mole numbers within the non-linear iteration loop is, especially at beginning, several orders of magnitude higher than the variation observed between successive values of the activity coefficients. The "strategy" of keeping constant, within the solver routine, the entities of second order variations, is also applied to the solvent activity, which is updated together with the activity coefficients.
This approach produces, without significant loss in efficiency, a Jacobian matrix whose expression is not specific to the model of activity correction chosen. An important advantage of this approach is to make possible for the user the implementation of a large variety of activity models in the dedicated module, 'outside' the Jacobian.
The Jacobian matrix, when the equilibrium equations are not substituted in the conservation equations, with Xi = ln(ni) :
	jw	jp≠jw	js
Eq[Ci]	[ %alpha_i^w e^{X_w} ]	[ %alpha_i^jp e^{X_jp} ]	[ %alpha_i^js e^{X_js} ]
Eq[As]	[1 - sum_{jp<>jw} %nu_{js,jp} ]	[ %nu_js^jp ]	I

As the module implementing the non-linear system and its Jacobian are clearly separated from the module in charge of the numerical resolution, the latter can be easily changed in order to test the efficiency of different types of numerical schemes. The scheme currently used is a Newton-Raphson iterative algorithm, with a line-search and backtracking method proposed by Kelley (2003). Other methods, implemented in ARXIM, can also be used in lieu of Kelley's Newton-Armijo method, for example methods described by Walker () and by Press et al. (1992).
### alternative approach
Using primary species as components for material balance, and formulating the system in terms of molalities, the equilibrium conditions can be represented in a rather compact form.
The same set of basis species, necessarily including the solvent H2O, is used to describe the stoichiometric relations between species and the formation of secondary species.
Working with molalities, there is no equation for the solvent, and material balance equations are written for primary solute species:
%PSI_{i in Ap/w} = m_i + %SIGMA_{j in As} %nu_j^i m_j - t_i ,
where ti is the "total molality " of primary species i.
Considering the secondary species S forming from basis species {H2O,P} by the reaction
%nu_j^w H_"2"O + %SIGMA_{i in Ap/w} %nu_j^i P_i rightarrow S_j " , " j in As
the corresponding equilibrium condition is
%gamma_j m_j = K_j prod_i {m_i}^{%nu_j^i} prod_i {%gamma_i}^{%nu_j^i} {a_w}^{%nu_j^w} ,or, with K_j^app= prod_i {%gamma_i}^{%nu_j^i} {a_w}^{%nu_j^w} ,
 m_j = K_j^app prod_i {m_i}^{%nu_j^i}
where the "apparent" equilibrium constant includes the activity coefficient product and solvent activity, which will be kept constant within the internal solution procedure.
Molalities of secondary species may be substituted directly in the material balance equations, giving a system of reduced size, whose Jacobian is
{partial %PSI_ip} over {partial m_jp} = %delta_ip^jp + [ %SIGMA_{k in As} %nu_k^ip %nu_k^jp m_k ] /m_jp , with m_k = K_k^app prod_i {m_i}^{%nu_k^i}
A condition for the solver to converge is that the primary species are those that actually dominate in the current system, otherwise the equation system is ill conditioned.
[next: examples of speciation runs]