## DYN: evolution of a water-rock system; a 0D dynamic cell
Computation of the equilibrium state of a water-rock system is essential for one of the main objects of the ARXIM project, which is to serve as the "chemical reactor" of a reactive transport code. It is used in this way in COORES (CO2 Reservoir Environmental Simulator), a code coupling ARXIM with SIMUSCOPP (Trenty, 2003), a code for multiphase transport in porous media. COORES-ARXIM is currently used for simulating scenarios of injection and sequestration processes of green house gases.
A "dynamic" run simulates the temporal evolution of a given volume of porous media as it is flushed by a given flux of fluid of given composition. It is thus a 0D reactive transport model, equivalent to the "continuous stirred tank reactor" (CSTR) model of chemical engineering.
The data at time t are the composition of the box (volume fractions and compositions of fluids and minerals) and the flux rate and composition of the injected fluid.
The main assumptions are that
► material transfer between fluid and minerals occurs only through dissolution – precipitation reactions which are kinetically controlled;
► an instantaneous equilibrium is realized among the aqueous species.
The variables comprise the mole numbers of fluid species in the box, n(1:nAq), and the mole numbers of mineral species, n(1:nM).
The system to be solved comprises three sets of equations:
▷ material balance of the independent components:
d over {dt} n_{Ci} + (Q_{Ci}^{"inj"} + Q_{Ci}^{"out"}) + R_{Ci} =0

▷ potential constraints among aqueous species (same as in speciation):
ln a_js " " - sum _{jp in Pr} {%nu_js^jp . ln a_jp } " " - %DELTA G_js^0 " "=0

▷ material balance on minerals:
d over {dt} n_m + R_m =0
#### → accumulation term
The accumulation term is the mole numbers of component [Ci] in the fluid in the box, computed as
n_{Ci}= sum_j %alpha_i^j n_j
#### → flux terms
The flux comprises an explicit input term, Qinj, imposed to the box as a volumetric Darcy flux, and an implicit output term Qout.
Thus, for each component:
► Q_{Ci}^{"inj"}= sum_j %alpha_i^j Q_j^{"inj"} = F_vol^{"inj"} times sum_j %alpha_i^j c_j^{"inj"} ,
where c_j^{"inj"}=n_j^{"inj"} over Vol_F^{"inj"} is the imposed concentration in the input fluid.

► Q_{Ci}^{"out"}= sum_j %alpha_i^j Q_j^{"out"} = F_vol^{"out"} times sum_j %alpha_i^j c_j ,
where c_j=n_j over Vol_F is the concentration in the box.
#### → reaction term

R_{C_i}= - sum_m %alpha_{i,m} size 10 {d over dt} n_m = - sum_m %alpha_{i,m} V_m ,
where Vm is the rate of precipitation / dissolution of mineral m, modeled as a sum of several reaction mechanisms:
V_m = (V_m^{d1}+V_m^{d2}+...+V_m^{dk}) + (V_m^{p1}+V_m^{p2}+...+V_m^{pl})
The following formalism (Lasaga et al, 1994), of common usage in water-rock simulation codes (Palandri & Kharaka, 2004), is used for the rate laws:
► precipitation rate:
size 12 { "if " %OMEGA_m<1 "; then " V_m^d = A_m times k_m(T) times prod_j (a_j)^{n_j} times (1-%OMEGA_m^%alpha)^%beta " ; else " V_m^d = 0 }
► dissolution rate:
size 12 { "if " %OMEGA_m>1 " ; then " V_m^p = A_m times k_m(T) times prod_j (a_j)^{n_j} times (%OMEGA_m^%alpha -1)^%beta " ; else " V_m^p = 0 }
where
▻ size 12 { %OMEGA_m = exp(-{ {%DELTA G_m} over RT }) }
measures the disequilibrium between mineral and the fluid, ΔGm being the molar free energy change attending the dissolution reaction of the mineral in the current fluid,
▻ A_m is the reactive surface area of the mineral,
▻ k_m(T) is its kinetic rate coefficient "far from equilibrium".
It depends on temperature according to an Arrhenius law:
k_m(T)= 10^{-pk_{T_ref}} exp(-E_{m,T_ref}*(1 over T - 1 over {T_ref}) /R)
where Em,Tref is the activation energy at temperature Tref.
▻ prod_j (a_j)^{n_j}
represents the influence of the fluid composition on the mineral rate, through the activity of aqueous species j that, depending on the sign of the exponent nj, act as catalyst or inhibitor.
Actually, in the current implementation, the different elementary rate laws share the same reactive surface Am and disequilibrium function and differ only in parameters km and in the nature of catalyzing and inhibiting species.
#### the relationship of surface to volume
Initial reactive surface areas, in terms of grain radius or of specific area, are given in the run's definition, along with initial mineral volume fractions.
It is possible to have several kinetic phases, pointing to the same thermodynamic species but having different textural properties, for example a coarse-grained quartz population and a fine-grained one.
To describe the relationship between the mole numbers of the kinetic phases in the reactive cell and their surface, each kinetic phase is considered as an ensemble of spherical grains of homogeneous radius (e.g. Lichtner, 1988).
In this "floating sphere" model, the reactive surface area for dissolution or precipitation of phase m at time step t is:
A_m= A_{m,0} ( n_m over {n_{m,0}} ) ^{2 over 3} , for precipitation and dissolution (option1)
where Am,0 and nm,0 are respectively the initial mole number and area of phase m.
This model, adapted to minerals growing or shrinking freely in a high porosity medium, becomes inconsistent at low porosity, when the grains come in contact with each other and part of their reactive surfaces becomes unaccessible.
Thus, optionally, introducing the porosity as a damping factor, the following dependence can be used for precipitation, in order to have the reactive surface tend to zero when porosity vanishes:
A_m= A_{m,0} (%phi over %phi_0)^{2 over 3} ( n_m over {n_{m,0}} ) ^{2 over 3} , for dissolution (option 2)
where φ and φ0 are the current and initial values of porosity.
For precipitation, instead of having the same relationship as for dissolution, we consider that it takes place not only on minerals of the same type, but on all the surface of the pores, and this results in the following surface / volume relationship:
A_m= A_{m,0} (%phi over %phi_0)^{2 over 3} , for precipitation (option2)

### implementation: the equation system
There are nF+nM unknowns, which are:
▶ nF mole numbers of aqueous species contained in the cell at time t, vYf(1:nF), or their logarithms, vXf(1:nF)= LOG(vYf(1:nF))
▶ nM mole numbers of mineral species contained in the cell at time t, vXm(1:nM)
For a given timestep Δt, the system to be solved comprises nF+nM equations, Ψ(1:nF+nM)=0, which can be distributed as three sets of equations, respectively
nC equations for the independent components,
nF-nC equations for the secondary species,
nM equations for the minerals
▶ nC equations implementing the mass balance constraints on the nC components:
%PSI_iC = ( 1 + U_{Darcy} over {%DELTA x} . %phi_f ) . SUM from j=1 to nAs ( %alpha_{iC,j} . vYf_j ) " (mole nrs in fluid from aqu'species)" newline " "- vF^{t- %DELTA t}_iC " (mole nr. in fluid at previous step)" newline " "- vF^"Inj"_iC . {U_{Darcy} } over {%DELTA x} . %DELTA t " (mole nr. injected)" newline " "+ SUM from j=1 to nMk ( %alpha_{iC,nAq+j} . vVm_j ) " (to/from minerals)"
In these equations, the porosity φf is not explicit, as it is a function of the minerals' mole numbers vXm.
▶ nF-nC equations describing the equilibrium between all nAq aqueous species, and eventually with a buffer component. Their formulation is equivalent to that used for static speciation calculations.
▶ nM rate equations for the nM mineral species currently "active":
%PSI_{nAq+j}= vXm_{j} - vMolM_j - %DELTA t . vVm_j
At beginning of a time step, the status of each mineral, is either dissolution, precipitation, or inaction, depending on its saturation state with respect to the fluid composition.
As already mentioned, Vmj, the rate for precipitation / dissolution of mineral j, is the product of three factors (VmS . VmAct . VmQsK), respectively functions of the mineral surface, the activities of species fluid, and the affinity of mineral – fluid reaction. These three factors have not the same degree of dependency on the dynamic evolution of the system. As a result, they are not necessarily updated at the same stage of the numerical scheme. Some of them, like the fluid activity factor, can be handled as explicit parameters, whereas others, especially the affinity factor, are better implicited, in order to allow the solution of large time steps.
### numerical method
To solve this system of non-linear equations, the modules for the residual system, for its jacobian, and for the convergence criteria are written according to the generic interface that makes them callable by the Newton-Raphson solvers already mentioned for the speciation issue.
Convergence of the Newton-Raphson algorithm is improved by using as initial values of the minerals mole numbers the values obtained by extrapolation according to their rates at the previous step. Extrapolation is also used for time step adjustment to prevent over-dissolution of a dissolving mineral.